## Slide 1
Part 2: NETPIE Introduction
(IoT Activity Kit)
by NETPIE.io
Customized and presented by Dr.Varodom Toochinda, Nov 2018, Last edited by Aimaschana Dec 2018

## Slide 2: NETPIE is……
IoT Platform facilitating real-time communications between things.
Has cloud data storage
Has configurable, ready-to-use dashboard
Has open-source library
Supports various
rogramming languages

## Slide 3: NETPIE คือ
From the perspective of developers,
NETPIE basically consists of
CLOUD + CLIENT LIBRARY

## Slide 4: Client Library
Client library of NETPIE is called Microgear library
It has four main functions
✔ Authorization (รับรอง)
✔ Authentication (อนุญาต)
✔ Communication (สื่อสาร)
✔ Coordination (ประสาน)

## Slide 5: How it works

## Slide 6: The mechanism inside….
Device authenticates with key+secret and gets access token.
Devices refer to each other with ALIAS.
Devices communicate via MQTT and HTTP protocols.
Microgear library acts as the middleware to NETPIE service.

## Slide 7: NETPIE - Where Things Chat
“Creativity is just designing
how THINGS connect.”

## Slide 8: Supporting Hardware and OS

## Slide 9: Supporting languages
C++(ESP8266, ESP32, Arduino, Particle)
Python
Javascript
Java
Node.js
C#
Android
Node-red

## Slide 10: Open-source library
NodeJS
Python
HTML5 Javascript
Arduino
ESP8266 Arduino
Android Studio
C#
JAVA
RESTful API
More coming soon…
https://github.com/netpieio
MQTT
HTTP

## Slide 11: NETPIE.io
https://netpie.io
Free 100 credits with unlimited time !

## Slide 12: Application ID
APPID
Key,Secret

## Slide 13: Application ID Defines Scope

## Slide 14: Key & Secret Are Credentials for Device Authentication
(Key, Secret) (Key, Secret) (Key, Secret)
Option 1: Share the same key for all devices

## Slide 15: Key & Secret Are Credentials for Device Authentication
(Key1, Secret1) (Key2, Secret2) (KeyN, SecretN)
Option 2: Use different keys for different devices

## Slide 16: Key Types
Device Key
Device key generates permanent token(s).
Recommended for physical devices where identities are persistent.
Session Key
Session key generates one-time token(s).
Recommended for logical devices e.g. web browser
Once disconnected from NETPIE, one-time token will be revoked

## Slide 17: ALIAS
ALIAS = nickname for your NETPIE “things”
MyBulb
MyBoard
MyApp
“MyBulb, are you turned on?”
“MyApp, now it is too dark”
“MyBulb, please turn on”

## Slide 18: NETPIE Resources
Application
Freeboard
Feed

## Slide 19: Hackable Open-source Dashboard
NETPIE Freeboard is open-source, configurable dashboard, in which
Datasource is retrieved and displayed in real time,
There are a variety of widgets for monitoring and controlling,
Web server is not required as it runs on client side.

## Slide 20: Data Storage Service
Feed
Stores time-series type of data
Up to 32 data fields per feed
Allowing up to 1 write per 15 seconds
Accessible through REST API

## Slide 21: Data Widget
Feed View
Widget in the dashboard to show live feed
Support plotting multiple datasets on the same chart
Customizable colors and styles

## Slide 22: NETPIE Freeboard Example

## Slide 23: Demo/Videos
Controlling RGB LED with 3 sliders on NETPIE Freeboard http://dewninjathai.blogspot.com/2017/07/freeboard-slider-esp8266-microgear.html
Reading from LSM9DS1 sensor (acceleration, angular rate and magnetic in 3D)
http://dewninjathai.blogspot.com/2018/04/lsm9ds1-netpie-freeboard.html

## Slide 24: NETPIE Mobile App

## Slide 25: Guide for how to install and use mobile app
Installation and instructions http://dewninjathai.blogspot.com/2018/04/netpie-app.html
Controlling robotic arm
http://dewninjathai.blogspot.com/2018/04/2-esp32-netpie.html
Testing push notification http://dewninjathai.blogspot.com/2018/05/push-notification-netpie-app.html

## Slide 26: Presence API
Device Status API
API notifying status of device (Online/Offline)
Available for both REST API และ Microgear method